THIS DOCUMENT HAS BEEN PREPARED ACCORDING TO THE PROVISIONS OF ARTICLE 136(3) “TRANSITIONAL MEASURES REGARDING EXISTING SUBSTANCES” OF REACH (REGULATION (EC) 1907/2006). IT IS NOT A PROPOSAL FOR A RESTRICTION ALTHOUGH THE FORMAT IS THE SAME

Annex XV dossier

Transitional Dossier

CAS No. 		100-41-4

EINECS No. 		202-849-4

IUPAC Name		Ethylbenzene

CONTENTS

Restriction proposal	3

Information on hazard and risks	4

1	identity of the substance and physical and chemical properties	4

1.1	Name and other identifiers of the substance	4

1.2	Composition of the substance	4

1.3	Physico-chemical properties	5

2	maNufacture and uses	7

3	classification and labelling	7

3.1	Classification in Annex I of Directive 67/548/EEC	7

3.2	Self classification(s)	8

4	environmental fate properties	9

5	Human health hazard assessment	9

6	Human health hazard assessment of physico-chemical properties	9

7	Environmental hazard assessment	10

8	PBT and VPVB assessment	10

9	Exposure assessment	10

10	Risk characterisation	10

Information on alternatives	10

11	Information on the risks to human health and the environment related to the manufacture of use of the alternatives	10

12	Availability of alternative, including the time scale	10

13	Technical and economical feasibility	10

Justification for restriction at Community level	11

14	Justification that action is required on the community-wide basis	11

15	Justification for the proposes restriction	11

socio economic assessment	12

other information	13

references	14

TABLES

Table 1: Summary of physico- chemical properties	5

FIGURES

EXAMPLES

Restriction proposal

CAS No. 		100-41-4

EINECS No.  		202-849-4

IUPAC Name		Ethylbenzene

Restriction proposal: None

Other Risk reduction measures see attached Risk Reduction Strategy.

Information on hazard and risks

1	identity of the substance and physical and chemical properties

1.1	Name and other identifiers of the substance

CAS No. 		100-41-4

EINECS No.  		202-849-4

IUPAC Name		Ethylbenzene

1.2	Composition of the substance

CAS Number:

EINECS Number:

IUPAC Name:

Molecular formula:

Structural formula:

Molecular weight:

Synonyms:

|  | 100-41-4 202-849-4 Ethylbenzene C8 H10 106 g/mol Ethylbenzol Benzene, ethyl- alpha.-Methyltoluene |
| --- | --- |

1.3	Physico-chemical properties

Vapour Pressure

The vapour pressure of a substance is defined as the saturation pressure above a solid or liquid substance. At the thermodynamic equilibrium, the vapour pressure of a pure substance is a function of the temperature only.

Vapour pressures in the range of 1 mm mercury column (1.333 hPa) at –9.8 °C to 760 mm (1013.25 hPa) mercury column at 136.2 °C are listed in the CRC Handbook of Chemistry and Physics (Lide, 1991-1992)

A value of 9.3 hPa at 20 °C is listed in the Auer Technikum (1988) which is a collection of common tables of several chemical compounds and is often used in laboratories. This value has been used for further calculations. 16 hPa at 30 °C and 46 hPa at 50 °C are also mentioned in the Auer Technikum. These values are also in good agreement with the values mentioned in the CRC Handbook.

A value of 9.33 hPa at 20 °C is mentioned by Verschueren (1983) and Duve et al. (1976) which supports the value of the Auer Technikum (1988).

Moreover Verschueren (1983) mentions a value of 16 hPa at 30 °C. This value is in good agreement with the Auer Technikum and the CRC Handbook.

Water Solubility

The water solubility of a substance is specified by its saturation concentration in pure water at a certain temperature, preferably at 20 °C.

A water solubility of 160 mg/l at 25 °C is mentioned in the CRC Handbook of Chemistry and Physics (Lide, 1991-1992). This value is in very good agreement with other values and has been used for further calculations therefore.

A value of 152 mg/l at 20 °C is mentioned by Tewari et al. (1982) and Verschueren (1983) whereas the value of 186.7 mg/l at 25 °C has been mentioned by Crookes and Howe (1991).

Partition Coefficient

The partition coefficient (Pow) is defined as the ratio of the equilibrium concentrations of a dissolved substance in a two phase system consisting of two largely immiscible solvents. In the case of n-octanol and water:

Pow = equilibrium cn-octanol : equilibrium cwater

The partition coefficient therefore is the quotient of two concentrations and is usually given in the form of its logarithm to base ten (logPow).

The logPow value at 25 °C was determined to be 3.13 by Tewari et al. (1982). This value was used for further calculations because the exact testing temperature was given. But nevertheless the value of 3.15 mentioned by Crookes and Howe (1991) and Verschueren (1983) correspond very well.

Table 1.1    Summary of physico-chemical properties

| Property | Value |  |
| --- | --- | --- |
| Physical state | liquid at 25 °C |  |
| Melting point | - 94.949 °C | Gerhartz (1987) |
| Boiling point (at 1013 hPa) | 136.186 °C | Gerhartz (1987) |
| Relative density | 0.8670 at 20 °C | Lide (1991-1992) |
| Vapour pressure | p(20 °C) = 9.3 hPa | Auer Technikum (1988) |
| Water solubility | 160 mg/l at 25 °C | Lide (1991-1992) |
| Partition coefficient n-octanol/water (log value) | 3.13 at 25 °C | Tewari et al. (1983) |
| Granulometry | not applicable (liquid) |  |
| Conversion factors |  |  |
| Flash point | 23 °C | CHEMSAFE |
| Autoflammability | 430 °C | CHEMSAFE |
| Flammability | highly flammable | CHEMSAFE |
| Explosive properties | not explosive | CHEMSAFE |
| Oxidizing properties | not oxidizing (structure) |  |
| Viscosity |  |  |
| Henry’s constant | 617 Pa m3/mol | calculated |
| Surface tension | 28.48 mN/m | Gerhartz (1987) |
| Index of refraction (nd) | 1.49588 at 20 °C 1.49320 at 25 °C | Gerhartz (1987) |

2	maNufacture and uses

See Risk Assessment Report

3	classification and labelling

3.1	Classification in Annex I of Directive 67/548/EEC

(Classification according to Annex I of the directive 67/548/EEC)

F				R 11		Highly flammable

Harmful			R 20		Harmful by inhalation

Proposal of the rapporteur

The entry in Annex I of directive 67/548/EEC does not yet include all categories of danger and qualifying risk phrases that have to be assigned according to the data presented. It is therefore proposed to amend the entry. The substance should be classified and labeled additionally with:

R 36/37/38	Irritating to eyes, respiratory tract and to skin

R48/20	Harmful: Danger of serious damage to health by prolonged exposure through inhalation

R 65				Harmful: May cause lung damage if swallowed

Proposed classification based on GHS classification

H319	Eye Irrit.2

H335	STOT Single3

H315	Skin Irrit.2

H373	STOT Rep.2

H304	Asp.Tox.1

3.2	Self classification(s)

4	environmental fate properties

See Risk Assessment Report Draft of November 2008.

5	Human health hazard assessment

See Risk Assessment Report Draft of November 2008.

6	Human health hazard assessment of physico-chemical properties

See Risk Assessment Report Draft of November 2008.

.

7	Environmental hazard assessment

See Risk Assessment Report Draft of November 2008.

8	PBT and VPVB assessment

9	Exposure assessment

See Risk Assessment Report Draft of November 2008.

10	Risk characterisation

See Risk Assessment Report Draft of November 2008.

Information on alternatives

11	Information on the risks to human health and the environment related to the manufacture of use of the alternatives

12	Availability of alternative, including the time scale

13	Technical and economical feasibility

Justification for restriction at Community level

14	Justification that action is required on the community-wide basis

None

Other measures see Risk Reduction Strategy.

15	Justification for the proposes restriction

15.1	Effectiveness

15.2	Practicality

15.3	Monitorability

socio economic assessment

other information

It is suggested to include here information on any consultation which took place during the development of the dossier. This could indicate who was consulted and by what means, what comments (if any) were received and how these were dealt with. The data sources (e.g registration dossiers, other published sources) used for the dossier could also be indicated here.

references

See Risk Assessment Report Draft of November 2008.

Annex

See Risk Assessment Report Draft of November 2008.

Risk Reduction Strategy Draft of November 2008