### AISE SPERC fact sheet - Industrial use in formulation of granular cleaning and maintenance products

| Section | Content |
| --- | --- |
| SPERC Title | Industrial use in formulation of granular cleaning and maintenance products |
| SPERC code |  |
|  | AISE SPERC 2.1.a.v2 Formulation of granular Detergents/ Maintenance Products: Regular & Compact (large scale) AISE SPERC 2.1.b.v2 Formulation of granular Detergents/ Maintenance Products: Regular & Compact (medium scale) AISE SPERC 2.1.c.v2 Formulation of granular Detergents/ Maintenance Products: Regular & Compact (small scale) |
| Scope |  |
|  | Covers the whole process of formulation as it occurs in the manufacturing of granular cleaning and maintenance products. This includes storing, mixing, packaging of substances (as part of preparations) and equipment cleaning, maintenance and associated laboratory activities. The SPERCs are relevant for operations which discharge their wastewater to treatment by a municipal sewage treatment plant. The SPERCs cover small, medium and large operations, which produce less than 1.000 tons, up to 10.000 tons or more than 10.000 tons of finished products per year, respectively. Substance Domain: All (see Narrative Description) |
| Related use descriptors |  |
|  | Main User Group: SU 3 |
|  | Sector of Use: SU10 |
|  | Environmental Release Class: ERC 2 |
|  | Process Categories: PROC1, PROC2, PROC3, PROC4, PROC5, PROC8a, PROC8b, PROC 9, PROC13, PROC 14, PROC15. |
|  | Product categories: PC 35 |
| Operational conditions |  | Operational conditions – Phrases |
|  | AISE 2.1.a.v2 | Process optimized for highly efficient use of raw materials. Indoor Use. |
|  | AISE 2.1.b.v2 | Process optimized for efficient use of raw materials. Indoor Use. |
|  | AISE 2.1.c.v2 | Process with efficient use of raw materials. Indoor Use. |
|  |  | Operational conditions - Free text background |
|  | AISE 2.1.a.v2 | General good practice: e.g. trained staff, spill protection including waste reuse. Closed automated process Closed transfer system Centralized process control Granular detergents are obtained by drying liquid slurries Reduced emissions to waste water due to e.g.: - Dry cleaning of equipment, use of Central or Peripheral Vacuum Cleaning - Cleaning involving so-called pigs in sub-processes involving liquid slurries. Reduced number of transfer and cleaning operations through e.g. : - Manufacturing of different products from one premix, to which certain ingredients are added to yield the final products. - Dedicated storage tanks for raw materials, premixes and final products. Residues of granular detergents recovered in cleaning steps at packaging or transfer lines are recycled into the slurries. |
|  | AISE 2.1.b.v2 | General good practice: e.g. trained staff, spill protection. Closed batch process Semi Closed transfer system Batch production of final product Granular detergents are obtained by drying liquid slurries. Reduced number of transfer and cleaning operations through e.g. : - Dedicated storage tanks for raw materials, and final products. Residues of granular detergents recovered in cleaning steps at packaging or transfer lines are recycled into the slurries. |
|  | AISE 2.1.c.v2 | General good practice: e.g. trained staff, spill protection. Batch process Granular detergents are obtained by drying liquid slurries. Batch production of final product. Residues of granular detergents recovered in cleaning steps at packaging or transfer lines are recycled into the slurries. |
| Obligatory onsite RMMs |  | RMM - Phrase | RMM-Efficiency (RESPERC) |
|  | AISE 2.1.a.v2 | No obligatory onsite RMM considered | 0 |
|  | AISE 2.1.b.v2 |  | 0 |
|  | AISE 2.1.c.v2 |  | 0 |
| Substance use rate |  | Phrase | Value (MSPERC) |
|  | AISE 2.1.a.v2 | Indicative worst case value for the substance use rate per site (MSPERC in kg/d) | 16700 |
|  | AISE 2.1.b.v2 |  | 4500 |
|  | AISE 2.1.c.v2 |  | 450 |
|  | Justification |
|  | MSPERC can be used by the registrant when starting the environmental assessment. MSPERC represents an indicative worst case value for the substance use rate per site. The MSPERC values have been estimated in dependence of the size of the operation, the number of days emitting, and the concentration of the substance in a finished product (i.e. mixture). See MSPERC-derivation in Appendix. |
| Days emitting |  | Phrase | Value (d) |
|  | AISE 2.1.a.v2 | Emission Days (days/year): | 250 |
|  | AISE 2.1.b.v2 |  | 250 |
|  | AISE 2.1.c.v2 |  | 250 |
| Release factors |  | Values (per pathway) |
|  |  | To air | To water | To soil | To waste |
|  | AISE 2.1.a.v2 | 0 | 0.0001 | 0 | 0 |
|  | AISE 2.1.b.v2 | 0 | 0.001 | 0 | 0 |
|  | AISE 2.1.c.v2 | 0 | 0.002 | 0 | 0 |
|  |  | Justification |
|  | Releases to Air: Releases of raw materials via volatilization of granulars are non-existent. For that reason, the study by Royal Haskoning (2009) does not consider to establish release factors for the use of fragrance materials in the manufacturing of detergent products. For that reason, the release factor is set to zero. Releases to water via wastewater: Releases to the wastewater can be the result of cleaning of mixing vessels, tubing, production/packaging lines with water. The spent cleaning water is discharged to the wastewater. The numbers that are presented in this SPERC are consistent with the emissions used as default in published Life Cycle Inventories (LCI) for the manufacturing of detergents and cleaners. These data were the basis for the A/B Tables of the EU Technical Guidance Document have been adopted as defaults in this SPERC. Releases to soil: Must be avoided. Releases to waste: Not relevant – no obligatory RMM which divert substances to waste. Residues of granular detergents recovered in cleaning steps at packaging or transfer lines are recycled into the slurries. Residues which cannot be recycled are disposed off as chemical waste. EU TGD 2003 Technical Guidance Document on Risk Assessment. Part II, Appendix1 A Table A2 (p 226) Franke et al., 1995 Ökobilanzierung- Sachbilanz für die Waschmittel-Konfektionierung Tenside Surf. Det, 32:(508-514 Royal Haskoning 2009 Review and evaluation of environmental emission scenarios for fragrance materials during compounding of perfume oils and formulation of consumer products (Research Institute for Fragrance Materials Ref.:9S3975.01/R0007/Nijm, 2009). |
| Optional risk management measures |  | Type of RMM | Efficiency |
|  | AISE 2.1.a.v2 AISE 2.1.b.v2 AISE 2.1.c.v2 | - pH adjustment / flocculation coagulation- | 30% |
| Narrative description | Industrial use in formulation of cleaning and maintenance products |
|  | This SPERC describes SPERC parameters relevant to the manufacturing of granular cleaning and maintenance products. Losses from the processes constitute losses of raw materials, which for economic reasons have to be avoided. Formulation of preparations requires optimized use of raw materials for inclusion into product. Typical emission reducing equipment/procedures in the detergent/cleaner plants may comprise: Spill protected areas (Dry) cleaning procedures with maximization of waste reuse in the process Collection of spills and handling by an external third party (typically via incineration) On-site physico-chemical pre-treatment of the waste water (e.g. via pH adjustment, flocculation/precipitation, sedimentation) Handling of the physico-chemical sludge by an external third party (typically via incineration) |
| Scaling | Scaling options are based on the comparison of the MSafe SPERC with MSite and changes due to RMM (RE) and/or dilution situation on site (q and GEffluent). |
|  | Scalable parameters | Parameter description | Values – SPERC /ES |
|  | MSafe SPERC, (kg/d) | Amount which can be safely used based on the SPERC | MSafe – outcome of chemical safety assessment |
|  | RETotal, SPERC | Removal efficiency assumed in the SPERC | 0 |
|  | qSPERC | Factor by which receiving surface water. dilutes the sewage after treatment | 10 |
|  | GEffluent, SPERC (m3/d) | Discharge rate of sewage. | 2.000 |
|  | Scaling condition |
|  |  | risk driven by wastewater treatment plant microbes [MSafe,SPERC x (1 – RETotal, SPERC )] / GEffluent, SPERC ( [MSite x (1 – RETotal, Site)] / GEffluent, Site |
|  |  | risk driven by freshwater/freshwater sediments, marine water/marine water sediments [MSafe,SPERC x (1 – RETotal, SPERC )] / (GEffluent, SPERC x qSPERC ) ( [MSite x (1 – RETotal, Site)] / (GEffluent, Site x qSite) |
|  | Site-specific parameters | Parameter description | Values – Site |
|  | MSite, (kg/d) | Amount which is actually used on-site | To be determined by Downstream User |
|  | RETotal, Site | Removal efficiency realized through RMMs on site |  |
|  | qSite | Factor by which receiving surface water dilutes the sewage after treatment |  |
|  | GEffluent, Site | Discharge rate of sewage from site |  |

### Appendix: MSPERC-Derivation

MSPERC can be used by the registrant when starting the environmental assessment. MSPERC-represents an indicative worst case value for the substance use rate per site. MSPERC is calculated according to: MSPERC  = MFinished x CSP x TEmission,SPERC -1 with CSP = Exemplary concentration of substance in finished product, MFinished = the amount of finished product manufactured (per year), TEmission,SPERC = number of days emitting. Typical parameters values are given in Table 1. MFinished -ranges correspond to the tonnage ranges of finished product as defined by Royal Haskoning (2009) for formulators. The MFinished –ranges are to help formulators find out which SPERC is relevant for their operation. MSPERC values in brackets correspond to MFINISHED production ranges. For MSPERC distinct values founded on expert estimation are provided, since these are recommended as starting values for environmental exposure assessments, provided no better information is available.

Table 1: Derivation of the default substance use rate MSPERC for Industrial use in formulation of liquid cleaning and maintenance products. The derivation is based on typical values of the operational conditions for the various applications covered by this SPERC.

| SPERC | Other Operational Conditions – Phrase | Operational Conditions – Values for selected parameters expressing the operational conditions for the SPERC ‘industrial use – formulation of granular cleaning and maintenance products. |
| --- | --- | --- |
|  |  | MSPERC in kg/d | TEmission, SPERC (days per year) | MFinished (t/y) | CSP |
| AISE 2.1.a.v2 | Process optimized for highly efficient use of raw materials. | 16700 (> 8000) | 250* | >10000 | 20% |
| AISE 2.1.b.v2 | Process optimized for efficient use of raw materials. | 4500 (800-8000) | 250* | 1000-10000 | 20% |
| AISE 2.1.c.v2 | Process with efficient use of raw materials. | 450 (<800) | 250* | <1000 | 20% |

### * Temission SPERC has been selected according to Royal Haskoning review on large and medium compounders (Royal Haskoning, 2009)

### SPERC 2.1.a.v2	AISE - Formulation of granular Detergents/ Maintenance Products: (large scale)

| Determinant Label | Quali-/ Quanti-tative | Value | Description of Value | Standard Phrase | Efficiency -if applicable |
| --- | --- | --- | --- | --- | --- |
| Equipment cleaning | Qual | Residues of granular detergents recovered in cleaning steps at packaging or transfer lines are recycled into the slurries. |  | Residues of granular detergents recovered in cleaning steps at packaging or transfer lines are recycled into the slurries. |  |
| General good practice | Qual | Trained staff, spill protection including waste reuse |  | Trained staff, spill protection including waste reuse |  |
| Indoor/outdoor use | Qual | Indoor Use |  | Indoor |  |
| Process efficiency | Qual | Process optimized for highly efficient use of raw materials (II) | Typical measures may include e.g. - Closed automated process and/or - Closed transfer system and/or - Centralized process control and/or - re-use of process grey water for cleaning optimized and/or automated systems for the transport and handling of raw materials, that minimize overall exposure levels and incidental spills Reduced number of transfer and cleaning operations through e.g. - Manufacturing of different products from one premix (masterbatch), to which certain ingredients are added to yield the final products. - Dedicated storage tanks for raw materials, premixes and final products Recovery of materials through e.g. - Recycling Residues of granular detergents in cleaning steps at packaging or transfer lines into the slurries. | Process optimized for highly efficient use of raw materials. |  |
| Type of Process | Qual. | Granular detergents are obtained by drying liquid slurries. |  | Granular detergents are obtained by drying liquid slurries. |  |
| Waste treatment | Qual. | Residues which cannot be recycled are disposed off as chemical waste. |  | Residues which cannot be recycled are disposed off as chemical waste. |  |

### SPERC 2.1.b.v2	AISE - Formulation of granular Detergents/ Maintenance Products: (medium scale)

| Determinant Label | Quali-/ Quanti-tative | Value | Description of Value | Standard Phrase | Efficiency -if applicable |
| --- | --- | --- | --- | --- | --- |
| General good practice | Qual | Trained staff, spill protection including waste reuse |  | Trained staff, spill protection including waste reuse |  |
| Type of process | Qual. | Granular detergents are obtained by drying liquid slurries. |  | Granular detergents are obtained by drying liquid slurries. |  |
| Indoor/outdoor use | Qual. | Indoor Use |  | Indoor |  |
| Equipment cleaning | Qual | Residues of granular detergents recovered in cleaning steps at packaging or transfer lines are recycled into the slurries. |  | Residues of granular detergents recovered in cleaning steps at packaging or transfer lines are recycled into the slurries. |  |
| Process efficiency | Qual. | Process optimized for efficient use of raw materials. | Typical measures may include e.g. - Closed batch systems and / or - Semi-closed transfer system and/or - Batch production of final product Reduced number of transfer and cleaning operations through e.g. - Dedicated storage tanks for raw materials, premixes and final products | Process optimized for efficient use of raw materials. |  |
| Waste treatment | Qual. | Residues which cannot be recycled are disposed off as chemical waste. |  | Residues which cannot be recycled are disposed off as chemical waste. |  |

### SPERC 2.1.c.v2	AISE - Formulation of granular Detergents/ Maintenance Products: (small scale)

| Determinant Label | Quali-/ Quanti-tative | Value | Description of Value | Standard Phrase | Efficiency -if applicable |
| --- | --- | --- | --- | --- | --- |
| General good practice | Qual | Trained staff, spill protection including waste reuse |  | Trained staff, spill protection including waste reuse |  |
| Type of process | Qual. | Granular detergents are obtained by drying liquid slurries. |  | Granular detergents are obtained by drying liquid slurries. |  |
| Indoor/outdoor use | Qual | Indoor Use |  | Indoor |  |
| Equipment cleaning | Qual | Residues of granular detergents recovered in cleaning steps at packaging or transfer lines are recycled into the slurries. |  | Residues of granular detergents recovered in cleaning steps at packaging or transfer lines are recycled into the slurries. |  |
| Process efficiency | Qual | Process with efficient use of raw materials. | Typically implemented measures for reducing emissions to waste water may include: - Closed batch systems | Process with efficient use of raw materials. |  |
| Waste treatment | Qual. | Residues which cannot be recycled are disposed off as chemical waste. |  | Residues which cannot be recycled are disposed off as chemical waste. |  |