### Cosmetics Europe / AISE SPERC fact sheet 
– Industrial use in formulation of solid cosmetic and home care products

| Section | Content |
| --- | --- |
| SPERC Title | Industrial use in formulation of solid cosmetic and home care products |
| SPERC code |  |
|  | Cosmetics Europe / AISE 2.3.a.v2 - Formulation of solid cosmetic and home care products (large scale) Cosmetics Europe / AISE 2.3.b.v2 - Formulation of solid cosmetic and home care products (medium scale) Cosmetics Europe / AISE 2.3.c.v2 - Formulation of solid cosmetic and home care products (small scale) |
| Scope |  |
|  | Covers the whole process of formulation as it occurs in the manufacturing of a solid cosmetic and home care products, e.g. body care soap, scented candles, shoe wax, etc. This includes storing, mixing, packaging of substances (as part of mixtures) and equipment cleaning, maintenance and associated laboratory activities. The SPERCs are relevant for operations which discharge their wastewater to treatment by a municipal sewage treatment plant. The SPERCs cover small, medium and large operations, which produce less than 1000 tons, up to 10,000 tons or more than 10,000 tons of finished products per year, respectively. Substance Domain: All (see Narrative Description) |
| Related use descriptors |  |
|  | Main User Group: SU 3 |
|  | Sector of Use: SU 10 |
|  | Environmental Release Class: ERC 2 |
|  | Process Categories: PROC1, PROC2, PROC3, PROC5, PROC8a, PROC8b, PROC 9, PROC14, PROC 15. |
|  | Product categories: PC 39 |
| Operational conditions |  | Operational conditions – Phrases |
|  | Cosmetics Europe / AISE 2.3.a.v2 | Process optimized for highly efficient use of raw materials., Indoor Use, Water-Based Process, Process with negligible volatilization |
|  | Cosmetics Europe / AISE 2.3.b.v2 | Process optimized for efficient use of raw materials, Indoor Use, Water-Based Process, Process with negligible volatilization |
|  | Cosmetics Europe / AISE 2.3.c.v2 | Process with efficient use of raw materials, Indoor Use, Water-Based Process, Process with negligible volatilization |
|  |  | Operational conditions - Free text background |
|  | Cosmetics Europe / AISE 2.3.a.v2 | General good practice: e.g. trained staff, spill protection including waste reuse. Advanced technology used in process e.g Closed automated process Closed transfer system Centralized process control Reduced emissions to waste water due to e.g.: - Dry cleaning of equipment (Use of absorbent materials including incineration of resulting solid waste) - Cleaning involving so-called pigs, CIP-System, etc. - Steam cleaning - Manual removal of residual products adhering to equipment (e.g. by manual scrubbing, vacuum cleaning, etc.) Reduced number of transfer and cleaning operations through e.g. - Manufacturing of different products from one premix, to which certain ingredients are added to yield the final products. - Dedicated storage tanks for raw materials, premixes and final products |
|  | Cosmetics Europe / AISE 2.3.b.v2 | General good practice: e.g. trained staff, spill protection. Technology used in process e.g Closed batch process Semi Closed transfer system Batch production of final product Reduced number of transfer and cleaning operations through e.g. Dedicated storage tanks for raw materials, and final products |
|  | Cosmetics Europe / AISE 2.3.c.v2 | General good practice: e.g. trained staff, spill protection. Used in process e.g Batch process Batch production of final product |
| Obligatory onsite RMMs |  | RMM - Phrase | RMM-Efficiency (RESPERC) |
|  | Cosmetics Europe / AISE 2.3.a.v2 | No wastewater treatment required. | 0 |
|  | Cosmetics Europe / AISE 2.3.b.v2 |  | 0 |
|  | Cosmetics Europe / AISE 2.3.c.v2 |  | 0 |
| Substance use rate |  | Phrase | Value (MSPERC) |
|  | Cosmetics Europe / AISE 2.3.a.v2 | Maximum daily site tonnage (kg/day): | 16,700 |
|  | Cosmetics Europe / AISE 2.3.b.v2 |  | 4,500 |
|  | Cosmetics Europe / AISE 2.3.c.v2 |  | 450 |
|  | Justification |
|  | MSPERC can be used by the registrant when starting the environmental assessment. MSPERC-represents an indicative worst case value for the substance use rate per site. The MSPERC values have been estimated in dependence of the size of the operation, the number of days emitting, and the concentration of the substance in a finished product (i.e. mixture). See MSPERC-derivation in Appendix. |
| Days emitting |  | Phrase | Value (d) |
|  | Cosmetics Europe / AISE 2.3.a.v2 | Emission Days (days/year): | 250 |
|  | Cosmetics Europe / AISE 2.3.b.v2 |  | 250 |
|  | Cosmetics Europe / AISE 2.3.c.v2 |  | 250 |
| Release factors |  | Values (per pathway) |
|  |  | To air | To water | To soil | To waste |
|  | Cosmetics Europe / AISE 2.3.a.v2 | 0 | 0.0005 | 0 | 0 |
|  | Cosmetics Europe / AISE 2.3.b.v2 | 0 | 0.001 | 0 | 0 |
|  | Cosmetics Europe / AISE 2.3.c.v2 | 0 | 0.002 | 0 | 0 |
|  |  | Justification |
|  | Releases to Air: Releases of raw materials via volatilization are quantitatively very low. For that reason, the study by Royal Haskoning (2009) does not consider to establish release factors for the use of fragrance materials in the manufacturing of detergent products. For that reason, the release factor is set to zero. Releases to water via wastewater: Releases to the wastewater can be the result of cleaning of mixing vessels, tubing, production/packaging lines with water. The spent cleaning water is discharged to the wastewater. The number for Cosmetics Europe 2.3.a.v2 is equal to that for large production of soap in the study by Royal Haskoning (2009). The Royal Haskoning data for small scale production of soap were adopted (in a conservative approach) for medium scale production according to Cosmetics Europe (Cosmetics Europe / AISE 2.3.b.v2). The number for small scale manufacturing of soaps according to Cosmetics Europe (Cosmetics Europe / AISE 2.3.c.v2) was extrapolated by the Cosmetics Europe and AISE sector expert teams based on the Royal Haskoning (2009) data. Releases to soil: Must be avoided. Releases to waste: Not relevant – no obligatory RMM which divert substances to waste. Royal Haskoning 2009 Review and evaluation of environmental emission scenarios for fragrance materials during compounding of perfume oils and formulation of consumer products (Research Institute for Fragrance Materials Ref.:9S3975.01/R0007/Nijm, 2009). |
| Optional risk management measures |  | Type of RMM | Efficiency |
|  | Cosmetics Europe / AISE 2.3.a.v2 Cosmetics Europe / AISE 2.3.b.v2 Cosmetics Europe / AISE 2.3.c.v2 | - Treat onsite wastewater (prior to receiving water discharge) to provide the required removal efficiency of  (%): | Efficiency to be specified depending on treatment technology available on site and substance properties. |
|  |  | - If discharging to domestic sewage treatment plant, no onsite wastewater treatment required. |  |
|  |  | - If discharging to domestic sewage treatment plant, provide the required onsite wastewater removal efficiency of  (%): |  |
|  |  | - Typical onsite wastewater treatment technology provides removal efficiency of  (%): |  |
|  |  | - Provide onsite wastewater removal efficiency of  (%): |  |
|  |  | Oil/ water separator |  |
|  | Typical emission reducing equipment/procedures in the cosmetic product plants may comprise: Spill protected areas (Dry) cleaning procedures with maximization of waste reuse in the process Collection of spills and handling by an external third party (typically via incineration) On-site physico-chemical pre-treatment of the waste water (e.g. via pH adjustment, flocculation/precipitation, sedimentation) manual removal of residual products adhering to equipment (e.g. by scrubbing, vacuum cleaning, etc.) Handling of the sludge by an external third party (typically via incineration) |
| Narrative description | Industrial use in formulation of solid cosmetic and home care products |
|  | For economic reasons, formulation of mixtures requires minimized losses of raw materials during the mixing and packaging of products. Losses of raw materials via volatilization are negligible. Significant losses to the environment can be the result of cleaning of mixing vessels, tubing, production/packaging lines. High viscosity products adhere more strongly to the walls of mixing vessels, tubing, production/packaging lines. They are less efficiently transferred into the packaging. Hence, emissions caused by equipment cleaning are higher and lower for high and low viscosity products, respectively. These losses occur irrespective of the physical-chemical properties of the substance employed in a cosmetic product. For that reason, this SPERC pertains to all substances. Technical comments Before treatment means: emissions as entering an on-site biological WWTP, or if absent, as leaving the site towards a municipal WWTP. It is assumed for simplicity that 1 kg cosmetic product (excl. water) represents ~ 1 kg COD. Actual average value for the chemical ingredients may range from 1-2. Emissions to soil or solid waste are not discussed here, as justified in IFRA (2009), these are considered negligible. Emissions to air are discussed above. |
| Scaling | Scaling options are based on the comparison of the MSafe SPERC with MSite and changes due to RMM (RE) and/or dilution situation on site (q and GEffluent). |
|  | Scalable parameters | Parameter description | Values – SPERC /ES |
|  | MSafe SPERC, (kg/d) | Amount which can be safely used based on the SPERC | MSafe – outcome of chemical safety assessment |
|  | RETotal, SPERC | Removal efficiency assumed in the SPERC | 0 |
|  | qSPERC | Factor by which receiving surface water. dilutes the sewage after treatment | 10 |
|  | GEffluent, SPERC (m3/d) | Discharge rate of sewage. | 2,000 |
|  |  | Scaling condition |
|  |  | risk driven by wastewater treatment plant microbes [MSafe,SPERC x (1 – RETotal, SPERC )] / GEffluent, SPERC ( [MSite x (1 – RETotal, Site)] / GEffluent, Site |
|  |  | risk driven by freshwater/freshwater sediments, marine water/marine water sediments [MSafe,SPERC x (1 – RETotal, SPERC )] / (GEffluent, SPERC x qSPERC ) ( [MSite x (1 – RETotal, Site)] / (GEffluent, Site x qSite) |
|  | Site-specific parameters | Parameter description | Values – Site |
|  | MSite, (kg/d) | Amount which is actually used on-site | To be determined by Downstream User |
|  | RETotal, Site | Removal efficiency realized through RMMs on site |  |
|  | qSite | Factor by which receiving surface water.dilutes the sewage after treatment |  |
|  | GEffluent, Site | Discharge rate of sewage. |  |

### Appendix: MSPERC-Derivation

MSPERC can be used by the registrant when starting the environmental assessment. MSPERC-represents an indicative worst case value for the substance use rate per site. MSPERC is calculated according to: MSPERC  = MFinished x CSP x TEmission,SPERC -1 with CSP = Exemplary concentration of substance in finished product, MFinished = the amount of finished product manufactured (per year), TEmission,SPERC = number of days emitting. Typical parameters values are given in Table 1. MFinished -ranges correspond to the tonnage ranges of finished product as defined by Royal Haskoning (2009) for formulators. The MFinished –ranges are to help formulators find out which SPERC is relevant for their operation. MSPERC values in brackets correspond to MFinished production ranges. For MSPERC distinct values founded on expert estimation are provided, since these are recommended as starting values for environmental exposure assessments, provided no better information is available.

Table 1: Derivation of the default substance use rate MSPERC for use in formulation of solid cosmetic and home care products. The derivation is based on typical values of the operational conditions for the various applications covered by this SPERC.

| SPERC | Other Operational Conditions – Phrase | Operational Conditions – Values for selected parameters expressing the operational conditions for the SPERC ‘industrial use – formulation of granular cleaning and maintenance products. |
| --- | --- | --- |
|  |  | MSPERC (kg/d) | TEmission,SPERC (days per year) | MFinished (t/y) | CSP |
| Cosmetics Europe / AISE 2.3.a.v2 | Process optimized for highly efficient use of raw materials. | 16700 (> 8000) | 250* | >10000 | 20% |
| Cosmetics Europe / AISE 2.3.b.v2 | Process optimized for efficient use of raw materials. | 4500 (800-8000) | 250* | 1000-10000 | 20% |
| Cosmetics Europe / AISE 2.3.c.v2 | Process with efficient use of raw materials. | 450 (<800) | 250* | <1000 | 20% |

### * Temission spERC has been selected according to Royal Haskoning review on large and medium compounders (Royal Haskoning, 2009)

### Appendix - Determinant Lists

### SPERC  Cosmetics Europe / AISE  2.3.a.v2: Formulation of solid cosmetic and home care products (large  scale)

| Determinant Label | Quali-/ Quanti-tative | Value | Description of Value | Standard Phrase | Efficiency -if applicable |
| --- | --- | --- | --- | --- | --- |
| Type of Process | Qual | Substance applied in aqueous process solution with negligible volatilization |  | Product applied in aqueous process solution with negligible volatilization. |  |
| Indoor/outdoor use | Qual | Indoor Use |  | Indoor |  |
| Equipment cleaning | Qual | Equipment cleaning with minimized emissions to wastewater | Typically implemented measures for reducing emissions to waste water may include: - Dry cleaning of equipment (Use of absorbent materials and vacuum cleaning including incineration of resulting solid waste) - Cleaning involving so-called pigs - Cleaning involving so-called "cleaning in place" (CIP System) - Steam cleaning and/or - Manual removal of residual products adhering to equipment (e.g. by manual scrubbing, vacuum cleaning, etc.) - use of two-liner systems (i.e. single use disposable reactor cover that is incinerated after use as solid waste) | Equipment cleaning with minimized emissions to wastewater |  |
| Process efficiency | Qual | Process optimized for highly efficient use of raw materials (II) | Typical measures may include e.g. - Closed automated process and/or - Closed transfer system and/or - Centralized process control and/or - re-use of process grey water for cleaning - optimized and/or automated systems for the transport and handling of raw materials, that minimize overall exposure levels and incidental spills - Reduced number of transfer and cleaning operations through e.g. - Manufacturing of different products from one premix (masterbatch), to which certain ingredients are added to yield the final products. - Dedicated storage tanks for raw materials, premixes and final products Recovery of materials through e.g. - Recycling Residues of granular detergents in cleaning steps at packaging or transfer lines into the slurries. | Process optimized for highly efficient use of raw materials. |  |

### SPERC  Cosmetics Europe / AISE  2.3.b.v2: Formulation of solid cosmetic and home care products (medium  scale)

| Determinant Label | Quali-/ Quanti-tative | Value | Description of Value | Standard Phrase | Efficiency -if applicable |
| --- | --- | --- | --- | --- | --- |
| Type of Process | Qual | Substance applied in aqueous process solution with negligible volatilization |  | Product applied in aqueous process solution with negligible volatilization. |  |
| Indoor/outdoor use | Qual | Indoor Use |  | Indoor |  |
| Equipment cleaning | Qual | Equipment cleaning with reduced emissions to wastewater | Typically implemented measures for reducing emissions to waste water may include: - Manual removal of residual products adhering to equipment (e.g. by manual scrubbing, vacuum cleaning, etc.) - use of two-liner systems (i.e. single use disposable reactor cover that is incinerated after use as solid waste) | Equipment cleaning with reduced emissions to wastewater |  |
| Process efficiency | Qual | Process optimized for efficient use of raw materials. | Typical measures may include e.g. - Closed batch systems and / or - Semi-closed transfer system and/or - Batch production of final product Reduced number of transfer and cleaning operations through e.g. - Dedicated storage tanks for raw materials, premixes and final products | Process optimized for efficient use of raw materials. |  |

### SPERC  Cosmetics Europe / AISE  2.3.c.v2: Formulation of solid cosmetic and home care products (small  scale)

| Determinant Label | Quali-/ Quanti-tative | Value | Description of Value | Standard Phrase | Efficiency -if applicable |
| --- | --- | --- | --- | --- | --- |
| Type of Process | Qual | Substance applied in aqueous process solution with negligible volatilization |  | Product applied in aqueous process solution with negligible volatilization. |  |
| Indoor/outdoor use | Qual | Indoor Use |  | Indoor |  |
| Equipment cleaning | Qual | Equipment cleaned with water, washing disposed of with wastewater. |  | Equipment cleaned with water, washing disposed of with wastewater. |  |
| Process efficiency | Qual | Process with efficient use of raw materials. | Typically implemented measures for reducing emissions to waste water may include: - Closed batch systems | Process with efficient use of raw materials. |  |